## Slide 1
Preliminary Design Review
;jgnfje tljgbnfiufdsanbjoiiewht[9 ho fdsgh FeatherCraft Integrated Structural Housing & Computer, Hardware Infofdafdsafrmation Processing Suite
Team: Barry Lurkey, Jorge Cervantes, Lewis Gilis, Evan Graser, Andrei Iskra,
Megan Howard, Taylor Maurer, Davis Peterson, Maggie Williams
Customer: Michael Brown
Advisor: Joe Tanner

## Slide 2: PROJECT MOTIVATION
Commercialization of International Space Station provides a launch opportunity not only to cubesats but larger 100 kg spacecraft
Spacecraft are launched on ISS cargo resupply missions, allowing for soft-stowed configuration and less stress on structure in launch environment
Surrey Satellite Technology US plans to offer the FeatherCraft system as a cost-effective platform for payloads of 45 kg or less.
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 3: PROJECT STATEMENT:
The 5 kg FeatherCraft structure shall provide support for a 100 kg total mass commercial spacecraft with reduced structural manufacturing time and materials cost, and enable the spacecraft to survive launch to and deployment from the ISS for a nadir facing missionJORGE=DICK.
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 4
FR 1 | The Feathercraft structure design shall be lightweight.
FR 2 | The Feathercraft structure design shall reduce manufacturing time and material cost from SST-US’s typical spacecraft estimates.
FR 3 | FeatherCraft Structure shall be designed to withstand a vibration table setting of 9.47 grms in soft-stowed configuration.
FR 4 | FeatherCraft Structure shall be designed to deploy from the Kaber Deployment Service.
FR 5 | FeatherCraft structure design shall interface with STS-US-provided spacecraft components and mission design.
FR 6 | An equivalent manufactured STM of the FeatherCraft structure design shall be used to demonstrate the feasibility of the FeatherCraft structure through a random vibration test to the requirements of SSP 50835.
FUNCTIONAL REQUIREMENTS:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 5: Structure Overview

## Slide 6: DESIGN OVERVIEW:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Nadir facing payload
Radiator
Solar Panels
Propulsion Plate
(Aerojet Rocketdyne)

## Slide 7: DESIGN OVERVIEW:
Carbon Fiber/
Aluminum Honeycomb Sandwich Panels
Extruded Carbon Fiber Columns
Customer-supplied
propulsion plate supports 12 kg propulsion unit
Tabbed interlocks allow easy integration
Middle plate supports
78 kg Avionics & Payload
All structural components are bonded together to avoid fasteners
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
30 in
30 in
19 in

## Slide 8: ASSEMBLY:
Start with Back Panel
Add Middle Plate and Corner Columns
Propulsion plate
and Propulsion unit
Side Panels bond on
Side Panels bond on
Integrate with
Avionics and Payload
Finish with
Upper Plate
Corner Joints bonded with overlapping face sheets
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Bond on Solar Panels to finish satellite integration

## Slide 9: Structure Feasibility

## Slide 10: Structure Feasibility
Materials are chosen to optimize mass
and maximize stiffness
  Feasible design will comply with mass requirement
  Structure will handle specified vibration tests
  Preliminary calculations assume quasi-static load
    Nominal average acceleration 1σ = 1.29 g (rms)

## Slide 11: Quasi-static load:
Assume: static load 1.4 g and 4σ dynamic load
F = m*a
F =M*g*1.4 + M*(4*1.29*g)
M = 100 kg; g = 9.81 m/s2
F = 6.9 kN
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 12: VIBRATION LOADING:
Axis: | Description: | Type of load: | Design Margin:
X | Tube – Plate | Shear | 5
 | Column | Buckling | 1
Y | Column | Bending | 6
 | Side panel | Bending | TBD
Z | Middle panel | Bending | 500
 | Mid panel tabs | Shear | 10
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Next:
Finite Element Model (FEM) analysis shall identify areas of max stress
Natural frequency shall be estimated
Detailed analysis for CDR
Major interfaces are analyzed to survive worst-case loading

## Slide 13: ADHESIVES:
Using adhesive for attaching all components and structure
  Worst loading case is 79.4 kPa
  Total adhesive surface area with a 0.005 in thickness yields ~0.25 qrt
  Picture of components on midplate
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 14: ADHESIVES:
Hysol EA 9394 Aerospace Adhesive
  Customer recommended
  1 qrt attainable at skygeek.com – $184.89
  1 qrt attainable at chemcenters.com - $210.00
  Bonded in composites lab, curing takes 24 hours with support tooling with full strength attained after 3-5 days
Scotch-Weld 2216 Epoxy
  Customer recommended, can be removed with heat
  1 qrt attainable at amazon.com – $275.74
  1 qrt attainable at ellsworth.com - $282.58
  Handling strength at 10 hours, cured for 7 days
Both have strength significantly higher than required for component mounting (79.4 kPa)
Property (25⁰C) | Hysol EA 9394 | Scotch-Weld 2216
Tensile Lap Shear | 28.9 MPa | 22.1 MPa
Tensile Strength | 46 MPa | 
Compressive Strength | 158.6 MPa | 
Density | 1360 kg/ | 1330 kg/
Mass needed | 0.288 kg | 0.282 kg
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 15: MASS BUDGET:
Chart: 
| Columns | Weight Reduced Panels | Adhesive | Margin
Sales | 0.726 | 3.63 | 0.3 | 0.344
Mass Limit: 5kg
Mass of Design: 4.7kg
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 16: MANUFACTURING:
Most weight relief and support tabs are 2D
  Achievable with Water Jet Cutter
    Available at the Physics machine shop
    Min. Radius = .006”
    Positional Tolerance < .005”
Panel edges still need milling
  Challenging
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
19 in
30 in
t = ½ in

## Slide 17: MANUFACTURING:
Machining of Panel Edges
  Required allow overlap of face sheet
  Fiber layer will likely fray and delaminate from core.
  Design options still being weighed
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Experimental Analysis of the Influence of Drill Point Angle
and Wear on the Drilling of Woven CFRPs (Feito, 2014)
t = ½ in

## Slide 18: EDGE CLOSE OUT:
Box Extrusion:
Use end mill or router table with a fly cutter to clear core
Used where panels interface with columns
Epoxy Fill In:
Use block to push core back from edge
Fill with Loctite TF 3056FR
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 19: RADIATOR FEASIBILITY:
Requirement: Use one 19” x 30” panel of the structure as a radiator capable of dissipating 100 W
Back of the Envelope performed using Stefan Boltzmann Law
Assumptions:
  Radiator panel is facing deep space (T∞ = 4 K)
  Panel temperature ~25°C (nominal operating temperature)
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 20: RADIATOR FEASIBILITY:
Proof of Feasibility and Area Calculation
Thermal Radiation – Stefan-Boltzmann Law
εC
qrad
T
Calculated Radiator Panel Surface Area: 460 in2
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Variable Definitions and Values:

## Slide 21: Testing OVERVIEW

## Slide 22: Test Facility:
Facility: Cascade Tek
  1530 Vista View Dr, Longmont, CO (~30min)
Cost: $1800 for 8 hour use of Vibration Table
  Currently factored into budget, may be donated by Surrey
  May require less than 8 hours, requires preliminary testing
Testing will occur in March with direct assistance from Cascade Tek test engineers
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 23: Random Vibration Test:
Profile specified by NASA Document:
  ISS Pressurized Volume Hardware Common Interface Requirements
Random Vibration Profile Characteristics
  20 Hz. – 2000 Hz. Frequency Range
  Random vibration loads specified for different frequencies
  Maximum Unattenuated Flight Envelope: 9.47 grms
  Maximum Attenuated Flight Envelope: 1.29 grms
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 24: Testing feasibility

## Slide 25
Structure will be wrapped in specified SECO-88 Bubble Wrap
  Attenuates Vibration Loading
Two ratchet straps will secure the structure to the table
  Hooked to ½” by 13 eyebolts (4), bolted directly to vibration table
Structure Mounting:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 26
  Stiff adhesive recommended by manual
    Superglue applied to bottom and pressed onto structure
  Signal transfer via shielded coaxial cable
ACCELEROMETER MOUNTING:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 27: Electrical Hardware OVERVIEW

## Slide 28: DAQ HARDWARE FBD:
Data Acquisition Board
Signal Conditioning
8-input S/H
ADC
Accel Channels (x8)
PC with Windows OS
(not delivered)
Hard Drive
Processor
Real-time Display
Digital
Analog
Power
Software
KEY
Data Acquisition Board
Signal Conditioning
8-input S/H
ADC
Accel Channels (x8)
5V
Micro
Controller
Board
Parallel Bit
Data Bus
5V
5V
Delivered
Designed
Replicate DAQ Boards for 60 Channels
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
USB Drive with DAQ Software
Accel Channels (x8)
Data Acquisition Board
Signal Conditioning
8-input S/H
ADC
120VAC
60 Hz
(wall outlet)
Switch
Power
Supply
24V

## Slide 29: Electrical Hardware FEASIBILITY

## Slide 30: ACCELEROMETERS:
Single Axis (PCB-333B30)
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Tri-axial (PCB-356A16)
Accelerometer | Buy | Rent
Single axis | $297 | $60/ month
Tri-axial | $931.50 | $200/ month
Resources:
Trudy Schwartz
Christine Buckler (ITLL) for barrowing accels and cables
The Modal Shop for renting accels for 30 days
Notes: Pictures from PCB.com

## Slide 31: ELECTRONICS SYSTEM:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 32: SIGNAL CONDITIONING:
Cost for Signal Conditioning:
  Printed Boards: PCB boards for $83, Advanced Circuits
  Assembly: Soldering Microcontroller for $X, Advanced Circuits
  Power Supply: $150 from Newark (BK 1550)
  Rest of the components: $3.00 per board
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 33: SIGNAL CONDITIONING:
Cost for the rest of the Signal Conditioning circuit:
  Resistors, Diodes & Capacitors: ~$1.50 per board
  Operational Amplifier: $0.70 each on Mouser
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 34: CIRCUIT:
Resources for Circuits:
  Trudy Schwartz and the Instrumentation Shop
  TIRESIAS project involved a similar accelerometer circuit
  PCB Piezoelectric and ADC manuals for circuit designs
  Altium Designer software available for student use
  PCB Designer Software through Advanced Circuits available
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 35: DATA TRANSFER TO PC:
Micro
Controller
(dsPIC33)
64-channel
simultaneous
sampling (200 KHz)
from charge amplifiers
I/O
USB to PC
Cmnd
Data
Logic
KEY
Parallel Bit
Data Bus
S/H – ADC (AD7606)
S/H – ADC (AD7606)
S/H – ADC (AD7606)
5 More ADCs
Convert
Convert
Convert
Chip Select
Chip Select
Chip Select
I/O
I/O
I/O
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
All channels sample and hold simultaneously by toggling convert pin

## Slide 36: DATA TRANSFER TO PC:
Micro
Controller
(dsPIC33)
64-channel
simultaneous
sampling (200 KHz)
from charge amplifiers
I/O
USB to PC
Cmnd
Data
Logic
KEY
Parallel Bit
Data Bus
S/H – ADC (AD7606)
S/H – ADC (AD7606)
S/H – ADC (AD7606)
5 More ADCs
Convert
Convert
Convert
Chip Select
Chip Select
Chip Select
I/O
I/O
I/O
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
First 8 data channels collected and stored.

## Slide 37: DATA TRANSFER TO PC:
Micro
Controller
(dsPIC33)
64-channel
simultaneous
sampling (200 KHz)
from charge amplifiers
I/O
USB to PC
Cmnd
Data
Logic
KEY
Parallel Bit
Data Bus
S/H – ADC (AD7606)
S/H – ADC (AD7606)
S/H – ADC (AD7606)
5 More ADCs
Convert
Convert
Convert
Chip Select
Chip Select
Chip Select
I/O
I/O
I/O
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Second 8 data channels collected and stored.

## Slide 38: DATA TRANSFER TO PC:
Micro
Controller
(dsPIC33)
64-channel
simultaneous
sampling (200 KHz)
from charge amplifiers
I/O
USB to PC
Cmnd
Data
Logic
KEY
Parallel Bit
Data Bus
S/H – ADC (AD7606)
S/H – ADC (AD7606)
S/H – ADC (AD7606)
5 More ADCs
Convert
Convert
Convert
Chip Select
Chip Select
Chip Select
I/O
I/O
I/O
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Next 8 data channels collected and stored.

## Slide 39: DATA TRANSFER TO PC:
Micro
Controller
(dsPIC24/33)
64-channel
simultaneous
sampling (200 KHz)
from charge amplifiers
I/O
USB to PC
Cmnd
Data
Logic
KEY
Parallel Bit
Data Bus
S/H – ADC (AD7606)
S/H – ADC (AD7606)
S/H – ADC (AD7606)
5 More ADCs
Convert
Convert
Convert
Chip Select
Chip Select
Chip Select
I/O
I/O
I/O
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Data sets transmitted to PC together
Process repeats

## Slide 40: Software OVERVIEW

## Slide 41: DESIGN:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Python, packaged as executable (.exe)
GUI created for user input
Implement already created python modules and libraries
Plot quasi-real-time PSD (power spectral density) plots
  Capability of saving data to excel (.xls)

## Slide 42
.exe
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Notes: 0. This is the external computer where data is saved and displayed. Right now

## Slide 43
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
PSD Plots
Notes: 2. After this the user will be able to enter limits, the save file location and channel number with a maximum of 60 channels.

## Slide 44
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Start
PSD Plots
Notes: 3. User then presses start to tell the microcontroller to initiate the data collection.

## Slide 45
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Raw Data Storage
Limit Checking
FFT
Start
PSD Plots
Notes: 3. This initiates the data collection, moving through limit checking, data storage, and the FFT. At this realtime data starts to populate the real-time plot.

## Slide 46
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Raw Data Storage
Limit Checking
FFT
Stop
PSD Plots
Notes: 4. Once data collection is finished, user will press stop, halting the communication from the microcontroller and the realtime plotting.

## Slide 47
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Raw Data Storage
Limit Checking
FFT
Stop
“Save report? (Y/N)” Query
Export to Excel ‘.xls’
PSD Plots
Notes: 4. Once data collection is finished, user will press stop, halting the communication from the microcontroller and the realtime plotting.

## Slide 48
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Raw Data Storage
Limit Checking
FFT
Stop
“Save report? (Y/N)” Query
Export to Excel ‘.xls’
PSD Plots
Notes: 4. Once data collection is finished, user will press stop, halting the communication from the microcontroller and the realtime plotting.

## Slide 49
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
GUI
Start/stop
Limits
Save file location
Channel #
Serial port interface module
USB
Already existing
Need to be built
Active data flow
User controlled
External Computer (Windows)
Raw Data Storage
Limit Checking
FFT
Stop
“Save report? (Y/N)” Query
Export to Excel ‘.xls’
PSD Plots
Notes: 4. Once data collection is finished, user will press stop, halting the communication from the microcontroller and the realtime plotting.

## Slide 50: Software FEASIBILITY

## Slide 51: Python Libraries Available:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Serial interface
  PySerial
FFT function
  NumPy
Excel implementation
  xlwings, xlsxwriter
PSD plotting
  matplotlib
Executable packager
  cx freeze
GUI Development
  Qt, tkinter
All libraries existence has been confirmed

## Slide 52: NEXT STEPS - SOFTWARE:
All tools needed are downloadable and installable
  Need to find out how they work – possible limitations
  If time allows start creating example scripts using new libraries
Start becoming familiar with python
  Some team members may need earlier start than others
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 53: CONCLUSION

## Slide 54: BUDGET:
Total Budget: $5000, Total Desired:$6277
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
Chart: 
| Structure | Data Acquisition System | Margin
Column1 | 2532 | 1945 | 523
Chart: 
| Structure | Vibration Testing | Margin
Column1 | 2532 | 1800 | 668
Chart: 
| Structure | Data Acquisition System | Vibration Testing | Margin
Column1 | 2532 | 521.5 | 1800 | 146.5

## Slide 55: PATH MOVING FORWARD :
Numeric Modeling
Familiarization with Python
Circuits?
EEF Award?
Vibe Testing Donation?
Final Component & Material Selection
Small Scale Component Testing
Software Development an Framework
Detailed Circuit Development
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 56: Back-up Slides

## Slide 57: Requirements: FR1
FR 1: The FeatherCraft structure design shall be lightweight.
  DR 1.1: Structural design mass shall be less than 5 kg.
    Source: Customer requirement. Increasing the structural mass beyond 5 kg would prevent SST-US from providing a profitable weight class of payloads
    Verification: Modeling and analysis, comparison with measurement of STM

## Slide 58: Requirements: FR2
FR 2: The Feathercraft structure design shall reduce manufacturing time and material cost from SST-US’s typical spacecraft estimates.
  DR 2.1: Structure design material cost shall be less than $20,000.
    Source: Customer requirement, SST-US typically expends $40,000 on a spacecraft material and this design shall reduce that metric by 50%.
    Verification: Budget analysis
  DR 2.2: Structure design manufacturing and assembling shall take less than 9 months.
    Source: Customer requirement, SST-US typically spends 18 months on spacecraft manufacturing and assembling and this design shall reduce that metric by 50%.
    Verification: Manufacturing estimates and analysis
  DR 2.3: Structure design manufacturing and building labor shall cost less than $80,000.
    Source: Customer requirement. This is a 50% reduction of SST-US’s typical manufacturing and building cost of $160,000 and will help the company meet the goal total price of $6 million.
    Verification: Budget estimates and analysis

## Slide 59: Requirements: FR3
FR 3: FeatherCraft Structure shall be designed to withstand a vibration table setting of 9.47 grms in a soft-stowed configuration.
  DR 3.1: FeatherCraft structure in launch configuration shall be designed to not be damaged by simulated launch environment, up to a 9.47 grms random vibration environment with safety factors as outlined in the GEVS ISS Pressured Volume Hardware Common Interface Requirements Document Rev C.
    Source : Customer requirement. To remain profitable, the FeatherCraft package needs to be reliable and provide a robust platform for their customers, as well as meet all NASA requirements for launch to the ISS.
    Verification: Vibration test executed on STM in FR 6 and measurement of STM before and after vibration test

## Slide 60: Requirements: FR4
FR 4: FeatherCraft Structure shall be designed to deploy from the Kaber Deployment Service.
  DR 4.1 FeatherCraft structure design including mounted components shall fit within the volume of 30”x30”x19”.
    Source: The spacecraft as a whole must be placed within the Kaber volume to be deployed and begin its mission. This volume ensures at least 2’’ of space between the spacecraft volume and the edge of the JEM airlock. Soft stowed as defined by GEVS ISS Pressured Volume Hardware Common Interface Requirements Document Rev C.
    Verification: Inspection of drawings, demonstration with measurement

## Slide 61: Requirements: FR5
FR 5: FeatherCraft structure design shall interface with SST-US-provided spacecraft components and mission design.
  DR 5.1: FeatherCraft structure design shall provide mounting positions on the three sides of the structure for one 30’’x30’’x0.125’’ solar panels of mass 2 kg and two 30’’x18.976’’x0.125’’ solar panel of mass 1.5 kg.
    Source: Customer requirement, knowing that this is a nadir-facing mission; the three sides that spend the most time facing the sun should have solar panels mounted on them. These sides will proven to always see sun through STK analysisare required by the customer to provide adequate power for interfacing components.
    Verification: Modeling and analysis in STK, STM demonstration in FR 5.
  DR 5.2: FeatherCraft structure design shall provide a mounting position for a 29.094’’x18.976’’x0.125’’ propulsion plate of mass 12 kg on Side 1.
    Source: Customer requirement. The propulsion plate design has been finalized, and its dimensions necessitate its mounting location.
    Verification: modeling and inspection of drawings, STM demonstration in FR 5
  DR 5.3 FeatherCraft structure design shall have an internal structural component equally bisecting the 19’’ height dimension to provide mounting capabilities to the avionics components and payload components.
    Source: Customer requirement. The mounting capabilities are necessary for the customer to assemble the spacecraft easily and safely. This bisecting structural component defines a payload bay and avionics bay so that a payload volume is defined for potential customers.
    Verification: Inspection of drawings, Test (measure STM)

## Slide 62: Requirements: FR5
  DR 5.4 FeatherCraft structure design shall dissipate up to 100 W of heat generated equally by avionics and payload bays at an operating temperature of -20 to 50 degrees C.
    Source: Customer requirement. The maximum power output is estimated by the customer to remain below 100W. The specifics of this analysis are presented in Section 4.1.4.
    Verification: Analysis
    DR 5.4.1: FeatherCraft structure design shall have a radiative material on the side facing deep space most often to dissipate heat.
      Source: Customer requirement, derived from DR 5.4. This shall be determined in the same STK analysis that determines which sides of the spacecraft experience the most direct sunlight over a year.
      Verification: Inspection of model, STK analysis
  DR 5.5 FeatherCraft structure design shall keep side 5 open.
    Source: Customer requirement, payload use and space for antenna(s) facing nadir.
    Verification: modeling, demonstration in STM
  DR 5.6 FeatherCraft structure design shall remain operational for five years in a space environment.
    Source: Customer requirement, the spacecraft bus will be advertised as a five-year mission.
    Verification: Analysis of structure material and assembly method for similarity to previous missions’ material heritage

## Slide 63: Requirements: FR6
FR 6: A manufactured STM of the FeatherCraft structure design shall be used to validate the design through a modal vibration sweep and a random vibration test to the requirements of SSP 50835.
  DR 6.1 STM shall be manufactured with sufficient similarity to the structural design such that it can be used for validation of the designed structure. It shall fulfill all of the requirements of the designed structure with the exception of the 5kg structural mass requirement, which may be exceeded.
    Source: Customer requirement. A physical test must be performed to provide a baseline of feasibility; this can only be proved if the STM is similar to the design. However, the materials of the STM are constrained to the FeatherCraft team budget.
    Verification: Analysis of materials
  DR 6.2 STM shall be tested on a vibration table for a vibration profile of 20-2000 Hz and up to a vibration table setting of 9.47 grms with each test lasting 60 seconds.
    Source: GEVS table 3.1.1.2.1.2.3.2-1 (Page 3-17 of ISS Pressured Volume Hardware Common Interface Requirements Document Rev C.) It is estimated by this document that with a vibration table setting of 9.47 grms, the bubble-wrapped structure should experience 1.29 grms.
    Verification: Inspection of test plan, test

## Slide 64: Requirements: FR6
  DR 6.3 STM shall support loads through vibration testing that are equivalent to the required loading of the designed structure.
    Source: Validation of FR 6
    Verification: Demonstration
    DR 6.3.1 STM shall have a provided mass analog propulsion plate of mass and size specified in 5.2 mounted to side 1
      Source: Validation of DR 5.2 and FR 5.
      Verification: Inspection
    DR 6.3.2 STM shall have provided solar panel mass analog plates mounted on sides determined from DR 5.1 with mass and size specified in DR 5.1
      Source: Validation of DR 5.1 and FR 6.
      Verification: Inspection
    DR 6.3.3 STM shall have an internal loading of 35 kg mounted inside the structure in the avionics bay to represent the avionics mass.
      Source: Validation of DR 5.3 and FR 6. This is the total mass of all spacecraft components SST-US intends to place inside the avionics bay.
      Verification: Measure mass, Inspection of drawings of vibration test configuration
    DR 6.3.4 STM shall have an internal loading of 47.5 kg mounted inside the structure in the payload bay to represent the payload mass.
      Source: Validation of DR 5.3 and FR 6. This is the SST-US provided estimate it will allow for payload mass.
      Verification: Measure mass, inspection of drawings of vibration test configuration

## Slide 65: Requirements: FR6
  DR 6.4: STM shall be wrapped in three layers of SECO 88 bubble wrap prior to testing.
    Source: Customer Requirement stemming from ISS Pressured Volume Hardware Common Interface Requirements Document Rev C. The test shall be performed with the STM in the flight configuration.
    Verification: Demonstration, inspection
  DR 6.5 FEM model shall be verified using structural accelerometer information.
    Source: Provides evidence for completion of FR 6 and allows data collection for later correlation to designed structure. The number of accelerometers necessary and their positons will be determined after the structural design is determined.
    Verification: Analysis of FEM model, inspection of drawings of vibration test configuration

## Slide 66: Requirements: FR6
  DR 6.6 A data acquisition and analysis system shall be designed and created for this test and further tests of structural STMs to validate structural properties.
    Source: Customer requirement, it will save the project money to own a data acquisition system, and this can be used for custom data collection and future tests
    Verification: Demonstration
    DR 6.6.1 Accelerometers determined by FR 6.5 shall be acquired for the testing of the STM, with one tri-axial accelerometer and one single-axis accelerometer retained by the design team.
      Source: Customer requirement. The number of accelerometers needed to validate the FEM model will be determined by the structure shape, and SST-US would like one accelerometer to base an expanded data acquisition system on if they could acquire it at the end of the project.
      Verification: Analysis of FEM model, demonstration
    DR 6.6.2 DAQ shall contain 60 channels for the possibility of 20 tri-axial accelerometer inputs.
      Source: Customer requirement, although the budget of the project limits the number of accelerometers to be used for the test in spring, future tests with 20 tri-axial accelerometers may be performed and data would be taken from all 20 at the same time.
      Verification: Analysis of circuitry and inspection of design drawings

## Slide 67: Requirements: FR6
    DR 6.6.3: Accelerometer data shall display in the form of power spectral density plots during each test
      Source: Customer requirement, safety for structure during test, real-time performance analysis
      Verification: Demonstration
    DR 6.6.4 Accelerometer data shall be saved during each test in an Excel-compatible format
      Source: Customer requirement, post-test analysis
      Verification: Demonstration
    DR 6.6.5 Accelerometer data shall be transferable via USB from the microprocessor collecting data to any personal computer running Microsoft Windows operating systems.
      Source: Customer Requirement. To prevent errors and wasted time, data should be easy to transfer to any of SST-US’ computers.
      Verification: Demonstration

## Slide 68: TRADITIONAL APPROACH:

## Slide 69: WEIGHT RELIEVED PANELS:

## Slide 70: COLUMNS:

## Slide 71: Digital Output Accelerometers:

## Slide 72: Build DAQ System w/ 1 Micro-Controller:

## Slide 73: Build DAQ System w/ Multiple Micro-Controllers:

## Slide 74: Analog to Digital Converter - FBD
- 16-bit simultaneous sampling
Bipolar input range 5V
Single 5V supply
Parallel port data output
Up to 200 kSPS on every channel

## Slide 75: Analog to Digital Converter - Operation
t1 = 45ns tconv = 4s tcycle = 5

## Slide 76: Accelerometer Mounting
Stud mounts impractical since they would require holes in structure

## Slide 77: Data sampling speeds
1. uC prompts ADC’s to convert data
2. 4s wait for conversion
3. Data retrieval requires 120 instruction cycles on parallel port, 1.7s
4. Data parsing requires 3 instruction cycles per channel, 180 cycles, 2.6
5. Data to PC via UART 11 bit words (8-E-1), 75
6. Total ~ 84s
7. 4KHz requires data sample every 0.25 ms, leaves 0.15ms margin
uC features:
- 17.5Mbps UART
- Parallel Bit Data Port
- 70 mega instruction cycles per second

## Slide 78: Structure Trade Study – Metric Definitions:
 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Material Cost: [kg] | 1 | 2 | 3 | 5 | 7.5 | 10 | 12.5 | 15 | 17.5 | 20
Mass [kg] | 4 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 9 | >10
Ease of Manufacturing: [hrs] | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
Ease of Analysis: | A monkey could do it | Plug and play | Very little effort required | Little effort required | Some effort required | Neutral | Effort required | Much effort required | Too much effort required | I quit

## Slide 79: Mechanical Design Trade Study:
 |  | Metalic Weight Relievd Panels | Honeycomb Weight-relieved Panels | Columns | Traditional Design
Criteria: | Weight: | Score: | Score: | Score: | Score:
Material Cost | 16% | 10 | 6 | 8 | 9
Mass | 35% | 2 | 10 | 9 | 2
Ease of Manufacturing | 26% | 7 | 6 | 7 | 5
Ease of Analysis | 23% | 8 | 8 | 6 | 8
Weighted Total: |  | 5.95 | 7.86 | 7.63 | 5.26

## Slide 80: Accelerometer Trade Study – Metric Definitions:
 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Unit Cost | < $1 | $1-$5 | $5-$10 | $10-$50 | $50-$100 | $100-$250 | $250-$500 | $500-$750 | $750-$1000 | >$1000
Reliability | 90-100% | 80-90% | 70-80% | 60-70% | 50-60% | 40-50% | 30-40% | 20-30% | 10-20% | 0-10%
Ease of interface to the structure | A baby can do it | Plug and play | Very little effort required | Little effort required | Some effort required | Neutral | Effort required | Much effort required | Too much effort required | I quit
Ease of design (including time invested) | Done! | Very easy | Easy | Somewhat easy | Neutral | Some what hard | Hard | Very hard | Uber hard | Impossible
Size/mass | 0 - 0.5g | 0.5 - 1g | 1 - 1.5g | 1.5 - 2g | 2 - 2.5g | 2.5 - 3g | 3 - 3.5g | 3.5 - 4g | 4 - 4.5g | >4.5g

## Slide 81: Accelerometer Trade Study:
 |  | Digital Accelerometers | Buy Piezoelectric Accelerometers | Rent Piezoelectric Accelerometers
Criteria: | Weight: | Score: | Score: | Score:
Unit Cost | 37.5% | 8 | 2 | 5
Reliability | 37.5% | 1 | 10 | 9
Ease of Interface to the Structure | 5% | 6 | 9 | 9
Ease of Design (including time invested) | 15% | 4 | 10 | 10
Size/mass | 5% | 8 | 2 | 2
Weighted Total: |  | 4.625 | 6.55 | 7.3

## Slide 82: Software Trade Study – Metric Definitions:
 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Cost | Free | $50-$100 | $100-$150 | $150-$200 | $200-$250 | $250-$300 | $300-$350 | $350-$450 | $400-$450 | >$450
Ease of implementation | A baby can do it | Plug and play | Very little effort required | Little effort required | Some effort required | Neutral | Effort required | Much effort required | Too much effort required | I quit
Resources Available | You can ask your mom for help | Courses taught on this, easy tutorials | Resident experts along with lower level resources | Profs., peers, online material | Peers, abundant online material | Peers, some online resources | Manuals, few online resources | Few online resources | Select books offer resources | No help from any resource

## Slide 83: Data Analysis Software Trade Study:
 |  | Python | Perl | LabVIEW
Criteria: | Weight: | Score: | Score: | Score:
Cost | 20% | 10 | 10 | 5
Ease of implementation | 60% | 6 | 4 | 7
Resources Available | 20% | 9 | 9 | 8
Weighted Total |  | 7.4 | 6.2 | 6.8

## Slide 84: DAQ Hardware – Metric Definitions:
 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
Manufacturing Difficulty | A baby can do it | Plug and play | Very little effort required | Little effort required | Some effort required | Neutral | Effort required | Much effort required | Too much effort required | I quit
Total Cost | <$20 | $20-$75 | $75-$150 | $150-$250 | $250-$375 | $375-$525 | $525-$700 | $500-$700 | $700-$1000 | >$1000
Complexity of Design | No work involved | Extremely Simple | Very Simple | Simple | Somewhat simple | Neutral | Somewhat Complex | Complex | Extremely Complex | Impossible
Reliability | 90-100% | 80-90% | 70-80% | 60-70% | 50-60% | 40-50% | 30-40% | 20-30% | 10-20% | 0-10%

## Slide 85: DAQ Hardware Trade Study:
 |  | Digital DAQ | Single | Multiple
Criteria: | Weight: | Score: | Score: | Score:
Manufacturing Difficulty | 10% | 7 | 4 | 3
Total Cost | 40% | 8 | 4 | 5
Complexity of Design | 10% | 5 | 4 | 3
Reliability | 40% | 1 | 9 | 8
Weighted Total |  | 4.8 | 6.0 | 5.8

## Slide 86: Adhesives Analysis
Largest load components – Communications subsystem
  10 kg, 160x135x60 mm
3 load cases – normal stress, shear, and peel
Normal and Shear Stress
  Assuming worst case of least surface area mounted,
Peel
  Worst surface is along long bonded edge (greatest moment induced stress)
  Assuming linear stress distribution
  Moment =
  Max induced stress=
  Max peel =

## Slide 87: Adhesives Analysis
Total adhesive needed
  Assuming largest surface area, total of avionics components is 0.467 .
  Payload surface area is not known, so assuming entire mid-plate is used for mounting, (30’’x30’’) this totals to 0.581 .
  Joints are assumed to use much less adhesive than payload and avionics mounting because of the small area, so an estimate of 25% the total payload and avionics surface area is assumed for a total surface area of 1.39 .
  Assumed thickness of 0.005’’ (standard as defined by MasterBonds.com) and adding a realistic margin of 0.001’’, the total volume of adhesive required is 0.224 qrt.
  For mass calculations, density is taken as 1360 kg/ thus

## Slide 88: INITIALIZATION:
Description
Run from an executable off a USB stick.
Created using libraries:
  cx freeze
  tkinter
  pyserial
Chirp μC to standby
Chirp μC
Open GUI
Standby for commands
User runs exe
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion
1. uC prompts ADC’s to convert data
2. 4s wait for conversion
3. Data retrieval requires 120 instruction cycles on parallel port, 1.7s
4. Data parsing requires 3 instruction cycles per channel, 180 cycles, 2.6
5. Data to PC via UART at 17.5 Mbps, 11 bit words, 75
6. Total ~ 84s
7. 4KHz requires data sample every 0.25 ms, leaves 0.15ms margin

## Slide 89: RUN TEST:
Description
Run from GUI button “Start.”
Created using libraries:
  pyserial
  matplotlib
  numpy
Chirp μC to gather data
Run FFT on nth data pull
Display alert window
Plot Power Spectral Density
User selects Start Button
Chirp μC
Gather Data from Serial Port
Check limits
Bad
Good
Repeat until stop command
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 90: STOP TEST:
Description
Run from GUI button “Stop.”
Created using libraries:
  pyserial
  matplotlib
  numpy
  xlsxwriter
Chirp μC to standby
Chirp μC
Prompt user to save report
Save raw data to csv
User selects Stop Button
Output plots and raw data to an excel file
yes
no
Reset GUI
Open Report file
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 91: RESET GUI:
Description
Run automatically after a test has been stopped.
Created using libraries:
  pyserial
  tkinter
Chirp μC to standby
Chirp μC
Flush data
Test terminates
Reset GUI
Standby for commands
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 92: SELECTED LIBRARIES:
Conclusion
Testing
Software
Electrical Hardware
Structure
Project Overview
Library: | Function: | Python Release:
cx freeze | Converts Python to MS Executable | 3.1 – 3.4
tkinter | GUI generation | 3.1 – 3.5
pyserial | Serial port communications | 3.0 – 3.4
numpy | Scientific computing package including FFT | 3.2 – 3.4
matplotlib | Graphic plotting capability | 3.1 – 3.4
xlsxwriter | Data read and write to MS excel format | 3.1 – 3.5

## Slide 93: PROJECT BUDGET – What We Want:
Chart: 
| Structure | Data Acquisition System | Vibration Testing
Column1 | 2532 | 1945 | 1800
Total Budget: $5000
Total Spent:
$ 6277
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 94: PROJECT BUDGET – Surrey Pays for Vibe:
Chart: 
| Structure | Data Acquisition System | Margin
Column1 | 2532 | 1945 | 523
Total Budget: $5000
Total Spent:
$ 3200
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 95: PROJECT BUDGET – EEF Approved
Chart: 
| Structure | Vibration Testing | Margin
Column1 | 2532 | 1800 | 668
Total Budget: $5000
Total Spent:
$ 4332
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 96: PROJECT BUDGET – Worst Case:
Chart: 
| Structure | Data Acquisition System | Vibration Testing | Margin
Column1 | 2532 | 521.5 | 1800 | 146.5
Total Budget: $5000
Total Spent:
$ 4853.50
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 97: Numerical Modeling
Challenges of using ANSYS to do in-depth analysis
  Good material properties
  Correct use of loads, boundary conditions, and element types
  Limitations of educational license (<40k elements)

## Slide 98: Material Properties
Using honeycomb properties provided from Hexcel corp.
  Orthotropic
Carbon Fiber more difficult
  Found that fabric orthotropic properties are not enough to describe buckling
  Used M55J fiber properties as generated by AJ Gemer, using a modeled simulated layup of alternating uni-directional cells=
LASP HyperDust Instrument CDR

## Slide 99: Applications of Boundary Conditions and Loads
Boundary Conditions are TBD on final model
For feasibility, used simple supports and uniform load distribution on middle panel
Used shell elements for face skin, 3d elements for core
  Concerned about 1-element through t
Deflections within 10% of analytical solution
Stresses within ~25%

## Slide 100: Getting around educational license
Having 3 layers of elements quickly creates too many elements.
Can use 1 layer of shell element (2D) and describe it’s material properties with a layered section
Deformation still within 16% of analytical
Stresses show ~no change

## Slide 101: Material Properties
Using honeycomb properties provided from Hexcel corp.
  Orthotropic
Carbon Fiber more difficult
  Found that fabric orthotropic properties are not enough to describe buckling
  Used M55J fiber properties as generated by AJ Gemer, using a modeled simulated layup of alternating uni-directional cells=
LASP HyperDust Instrument CDR

## Slide 102: CHARGE AMPLIFIER:
Project Overview
Structure
Electrical Hardware
Software
Testing
Conclusion

## Slide 103: Why 60 Channels?
Used as an estimate from Surrey until we are able to perform a modal analysis test on the structure.
Project Overview
Structure Overview
Electrical Hardware Overview
Structure Feasibility
Electrical Hardware Feasibility
Software Overview
Software Feasibility
Testing

## Slide 104: TITLE:
Project Overview
Structure Overview
Electrical Hardware Overview
Structure Feasibility
Electrical Hardware Feasibility
Software Overview
Software Feasibility
Testing

## Slide 105: TITLE:
Project Overview
Structure Overview
Electrical Hardware Overview
Structure Feasibility
Electrical Hardware Feasibility
Software Overview
Software Feasibility
Testing

## Slide 106
Project Overview
Structure Overview
Electrical Hardware Overview
Structure Feasibility
Electrical Hardware Feasibility
Software Overview
Software Feasibility
Testing

## Slide 107: TITLE:
Thing 1: | Thing 2: | Thing 3: | Thing 4: | Thing 5:
Project Overview
Structure Overview
Electrical Hardware Overview
Structure Feasibility
Electrical Hardware Feasibility
Software Overview
Software Feasibility
Testing

## Slide 108: SECTION HEADER